## Slide 1
WELCOME
OBSERVATIONS of Hazardous audit committee installation at Ammonia storage,Chlorination Section,Acid tanks and Gas storage areas
Visit No-2.

## Slide 2: Ammonia storage section
Steps involved in the audit
Verification of inspection report of all pressure tanks of refrigeration system; found normal.
Instrumentation Bypass logics of all equipments checked found normal.
Safety accessories, availability and status checked found normal.
Wind Socks at 03 different locations as per HAZOP recommendation found in intact condition.

## Slide 3
Ammonia gas Detectors at two different locations checked and verified.
Chlorination installation and chlorine scrubber of ammonia CT section has been checked thoroughly and Loopholes are identified.
Through field inspections and identifications of hazards and loopholes along with the status of previous audit report its compliance and new points are shown in the following slides with pictorial views.

## Slide 4: Pipeline support structures of Ammonia Tank-B
Now, the corroded Column Base is corrected and proper strengthening done.
Then, Condition of the foot base of vertical column at Tank-B.

## Slide 5: Ammonia Tank-B
Now,Strengthening Job is under Progress, Column is enforced with new plates
Then, Condition of the Columns

## Slide 6
Now, new support beam installed
Then, corroded support beam in pipe rack near tank-B
Pipe Rack at Ammonia Tank-B

## Slide 7: Compressor House
Then, condition of the slabs in compressor house was in disorganized condition
Now, the slabs are in organized condition

## Slide 8
Shed for pilot ignition Corrected

## Slide 9: New Points Marked at Ammonia Storage area
Shoe support for 30 “ Vapor ammonia line in TANK-C is dislocated. The same is to be fixed

## Slide 10
Support Channel of Walkway Path is highly Corroded and requires
Replacement in Ammonia Tank-C

## Slide 11
Algae contamination in the insulation line is observed, replacement of insulation is required

## Slide 12
One strip is missing in the staircase of Ammonia Tank-C

## Slide 13
Materials in the mechanical store room is found in disorganized manner at Ammonia Storage

## Slide 14
Vegetation is to cleared around the pipelines

## Slide 15
Concrete slab is damaged at the base floor of Ammonia flare stack

## Slide 16
Proper support missing in the vent line at ammonia Storage section.

## Slide 17: Chlorination installation at Ammonia Storage
MSDS board installation is required.
Do’s and don’t board is to be installed.
Safety precaution board is required.
Wind Sock in the vicinity area is to be installed.
Chlorine scrubber system is not working due to leakage in the caustic lye solution storage tank, the same is to be corrected.

## Slide 18: Chlorine installation at Raw Water treatment Plant
Now, The Ton Cylinders found stacked as per IS standard.
Then, the ton cylinders were not stacked as per IS standard.

## Slide 19: Chlorination system at TG Cooling Tower.
MSDS board installation is required.
Hose arrangement at the vicinity of chlorination house is required.
Do’s and Don’t board in both hindi and oriya language should be installed.

## Slide 20
Chlorine scrubber not placed properly and unwanted materials found in the chlorine house at TG cooling tower.

## Slide 21
Proper Cleaning is required at pumping and roadways at FO tank area

## Slide 22
Staircase of Sulphuric Acid is badly corroded

## Slide 23
Base plate of sulphuric Acid Tank is corroded, proper action is required

## Slide 24
Dyke Wall of Sulphuric Acid tank requires repairmen

## Slide 25
Bolt of the bellow flange is highly corroded at sulphuric
Acid tank

## Slide 26
Effluent/Drain Acid pumping arrangement at sulphuric Acid Tank Area is missing

## Slide 27
Pipeline Support at sulphuric Acid export tank is improper

## Slide 28
Vegetation growth observed at the periphery of Dyke wall at sulphuric acid export tank

## Slide 29
Effluent/Drain Acid pumping arrangement is missing at Sulphuric Acid Export Tank

## Slide 30
Tank Pitting and nearby wetness observed in sulphuric Acid Tank-A

## Slide 31
Unwanted Scrap materials are falling at Phosphoric Acid Export tank

## Slide 32
Unwanted
Scrap materials
Are placed at
Phosphoric Acid
Tank Base

## Slide 33
Corrosion and pitting observed at Fluorosilicic Acid Tank

## Slide 34
Proper Acid brick lining is required at Flurosilic Acid Tank area

## Slide 35
Proper Drainage system is missing for overflow line of Flurosilic Acid tank

## Slide 36
Walkway rail and gratings were badly corroded, the same has been replaced with SS
Then
Now

## Slide 37
Then Vegetation growth Was observed at Phosphoric Acid Export Tank
Now they are properly removed
Then
Now

## Slide 38
Previously Gas Cylinders are not placed properly, Now it is properly placed and chained.
Then
Now